;USKI-5 PROGRAM(B)PROVIDES SEPARATE CW AND PTT INPUTS AND OUTPUTS WITH "SEND" MONITORING FROM RIG AND INHIBIT CAPABILITY PLUS DIFFERENT TIMING DELAYS FOR CW AND PTT MODES

;REFER TO THE USKI-5 USER MANUAL FOR PROPER INPUT AND OUTPUT CONNECTIONS TO THE SEQUENCER

;ALL DELAYS ARE IN MILLISECONDS (ms)

symbol CW_START_DEL_1 = 8 * 0			;output 1 CW start delay
symbol CW_START_DEL_2 = 8 * 0			;output 2 CW start delay
symbol CW_START_DEL_3 = 8 * 0			;output 3 CW start delay
;symbol CW_START_DEL_4 not used in this program, output 4 reserved for PTT operation
symbol CW_START_DEL_5 = 8 * 0			;output 5 CW start delay

symbol CW_END_DEL_5 = 8 * 0			;output 5 CW end delay, compensation for start delays, often sum of START_DEL_1, 2, 3, and 5
;symbol CW_END_DEL_4 not used in this program, output 4 reserved for PTT operation
symbol CW_END_DEL_3 = 8 * 0			;output 3 CW end delay
symbol CW_END_DEL_2 = 8 * 0			;output 2 CW end delay
symbol CW_END_DEL_1 = 8 * 0			;output 1 CW end delay

symbol PTT_START_DEL_1 = 8 * 0		;output 1 PTT start delay
symbol PTT_START_DEL_2 = 8 * 0		;output 2 PTT start delay
symbol PTT_START_DEL_3 = 8 * 0		;output 3 PTT start delay
symbol PTT_START_DEL_4 = 8 * 0		;output 4 PTT start delay 
;symbol PTT_START_DEL_5 not used in this program, output 5 reserved for CW operation		

;symbol PTT_END_DEL_5 not used in this program, output 5 reserved for CW operation			
symbol PTT_END_DEL_4 = 8 * 0			;output 4 PTT end delay
symbol PTT_END_DEL_3 = 8 * 0			;output 3 PTT end delay
symbol PTT_END_DEL_2 = 8 * 0			;output 2 PTT end delay
symbol PTT_END_DEL_1 = 8 * 0			;output 1 PTT end delay

pullup on						;turns on pullup resistors for all inputs
setfreq M32						;overclock to 32 MHz

main:

initialize:						;initialize outputs upon power up. low = OUTPUT OPEN, high = OUTPUT CLOSED
	low B.1
	low B.2
	low B.3
	low B.4
	low B.5	

standby:						;waits in this loop until cw or ptt input
	setint %00000000,%00000100		;sets interrupt on input C.2 (jack J2R)
	if pinC.2 = 0 then goto standby	;checks for interrupt on C.2(J2R closed)		
	bit0 = 0					;clears any interrupt flag, if necessary
	if pinC.1 = 0 then goto cwstart	;checks for CW key input C.1(J1T closed)	
	if pinC.0 = 0 then goto pttstart	;checks for PTT input C.0(J1R closed)
	if pinC.3 = 0 then goto safe		;checks for accidental direct keying of rig
	goto standby
safe:							;run if xmtr/xcvr accidentally keyed or PTT directly
	high B.1
	high B.2
	high B.3
	if pinC.3 = 0 then goto safe
	pause PTT_END_DEL_3
	low B.3
	pause PTT_END_DEL_2
	low B.2
	pause PTT_END_DEL_1
	low B.1
	goto standby
	
cwstart:						;beginning of CW start procedure
	
	pause CW_START_DEL_1			;output 1 CW start delay
	if pinC.1 = 1 then goto standby	;checks if key up 
	if bit0 = 1 then goto standby		;checks if interrupt occurred during pause 1, if so goes to standby
	high B.1					;switches output 1
	pause	CW_START_DEL_2			;output 2 CW start delay
	if pinC.1 = 1 then goto cwend1	;checks if key up
	if bit0 = 1 then goto cwend1		;checks if interrupt occurred during pause 2
	high B.2					;switches output 2
	pause CW_START_DEL_3			;output 3 CW start delay
	if pinC.1 = 1 then goto cwend2	;checks if key up
	if bit0 = 1 then goto cwend2		;checks if interrupt occurred during pause 3
	high B.3					;switches output 3
	
	;output 4 excluded, used only by PTT routine in this program
	
	pause CW_START_DEL_5			;output 5 CW start delay
	if pinC.1 = 1 then goto cwend3	;checks if key up
	if bit0 = 1 then goto cwend3		;checks if interrupt occurred during pause 5
	high B.5
	goto keydown

semiloop:						;for key down from semibrkin loop
	setint %00000000,%00000100		;sets interrupt on input C.2 (jack J2R)
	pause CW_START_DEL_1
	if bit0 = 1 then goto cwend5		;monitors for interrupt 
	pause CW_START_DEL_2
	if bit0 = 1 then goto cwend5		;monitors for interrupt 
	pause CW_START_DEL_3
	if bit0 = 1 then goto cwend5		;monitors for interrupt 
	high B.5					;switches output 5

	
keydown:						;CW keydown hold loop
	setint %00000000,%00000100		;sets interrupt on input C.2 (jack J2R)
	if bit0 = 1 then goto cwend5		;monitors for interrupt 
	if pinC.1 = 0 then goto keydown	;loops here while CW key (C.1)is low
		
	pause CW_END_DEL_5			;output 5 CW end delay		
	low B.5					;unswitches output 5
		
semibrkin:						;loops here for semi-breakin operation
	setint %00000000,%00000100		;sets interrupt on input C.2 (jack J2R)
	if bit0 = 1 then goto cwend5
	if pinC.1 = 0 then goto semiloop	;if key down, goes to semiloop
	if pinC.3 = 0 then goto semibrkin

cwend5:
	low B.5
	pause CW_END_DEL_3			;output 3 CW end delay
	
	;output 4 excluded, used only by PTT routine in this program

cwend3:	
	if pinC.3 = 0 then goto cwend3	;checks for release of "send" from xmtr/xcvr
	low B.3					;unswitches output 3
	pause CW_END_DEL_2			;output 2 CW end delay

cwend2:	
	low B.2					;unswitches output 2
	pause CW_END_DEL_1			;output 1 CW end delay

cwend1:	
	low B.1					;unswitches output 1
	goto standby				;go back to standby

pttstart:						;beginning of TX start procedure
	
	pause PTT_START_DEL_1			;output 1 PTT start delay
	if pinC.0 = 1 then goto standby
	if bit0 = 1 then goto standby		;checks if interrupt occurred during pause 1, if so goes back to standby
	high B.1					;switches output 1
	pause	PTT_START_DEL_2			;output 2 PTT start delay
	if pinC.0 = 1 then goto pttend1
	if bit0 = 1 then goto pttend1		;checks if interrupt occurred during pause 2
	high B.2					;switches output 2
	pause PTT_START_DEL_3			;output 3 PTT start delay
	if pinC.0 = 1 then goto pttend2
	if bit0 = 1 then goto pttend2		;checks if interrupt occurred during pause 3
	high B.3					;switches output 3
	pause PTT_START_DEL_4			;output 4 PTT start delay
	if pinC.0 = 1 then goto pttend4
	if bit0 = 1 then goto pttend4		;checks if interrupt occurred during pause 4
	high B.4					;switches output 4
	
	;output 5 excluded, only used by CW routine in this program
	
ptthold:						;holds in this loop while PTT on
	setint %00000000,%00000100		;sets interrupt on input C.2 (jack J2R)
	if bit0 = 1 then goto pttend4		;checks for interrupt	
	if pinC.0 = 0 then goto ptthold	;loops while PTT input continues
	pause PTT_END_DEL_4			;output 4 PTT end delay
	
	
	;output 5 excluded, only used by CW routine in this program

pttend4:
	low B.4					;unswitches output 4
	if pinC.3 = 0 then goto pttend4	;checks for release of "send" from xmtr/xcvr		
	pause PTT_END_DEL_3			;output 3 PTT end delay
pttend3:	
	low B.3					;unswitches output 3
	pause PTT_END_DEL_2			;output 2 PTT end delay

pttend2:	
	low B.2					;unswitches output 2
	pause PTT_END_DEL_1			;output 1 PTT end delay

pttend1:	
	low B.1					;unswitches output 1
	goto standby				;go back to standby

	
interrupt:						;interrupt routine
	
	bit0 = 1					;set interrupt flag on
	return					;return to point where interrupt occurred